## Slide 1
Safer E-Waste Dismantling in Solapur
A Review of Benign Solvents, Less Hazardous Synthesis Methods,
and Design for Degradation Principles
Applied Chemistry for Engineers (AS-1201)
B.Tech CSE-AIML | Solapur, Maharashtra, India
13 march 2026
Gafur Subhedar,
Sudarshan Bhadule,
vishvajit shinde

## Slide 2
Agenda
01
Introduction & Research Problem
02
Literature Review & Background
03
Methodology
04
Results: Metal Recovery Efficiency
05
Results: Comparative Analysis
06
Data Table: Key Studies
07
Discussion & Analysis
08
Conclusion
09
References

## Slide 3
Introduction & Research Problem
"How might we develop safer e-waste dismantling processes in Solapur using benign solvents, less hazardous synthesis methods, and design for degradation principles?"
Global e-waste projected to reach 82 million tonnes by 2030
India is the 3rd largest e-waste generator (2M+ tonnes/year)
Over 95% handled by informal sector without safety equipment
Solapur's informal workers exposed to Pb, Cd, Hg, Cr daily
Green chemistry offers viable, scalable alternatives
82M
Tonnes e-waste
by 2030
>95%
Informal sector
processing in India
3-5%
Annual growth rate
of global e-waste
<5%
Formal recycling
capacity in India

## Slide 4
Literature Review & Background
2001
Brandl et al. — bioleaching proof of concept from PCBs
2008
Cui & Zhang — metallurgical recovery methods review
2010
Ilyas et al. — 80%+ copper via bacterial bioleaching
2014
Smith et al. — foundational DES chemistry (5,400+ citations)
2019
Tran et al. (Nature Energy) — 90%+ Li/Co recovery via DES
2021
Pathak et al. — fungal bioleaching at near-neutral pH
2024
Hubbard et al. (Nature Sustainability) — vitrimer PCBs
2026
Amusa et al. — 100% Li, 99.6% Co DES recovery confirmed
Deep Eutectic Solvents (DES)
Choline chloride + HBD systems recover 80-95% gold, 99.6% cobalt under ambient conditions. Biodegradable and food-grade precursors. 40-60% lower GWP than pyrometallurgy.
Bioleaching Systems
Bacterial: >80% Cu, strict pH 1.5-2.5. Fungal (Aspergillus niger): 85% Cu at near-neutral pH — more accessible for informal settings without acid infrastructure.
Mechanochemical Processing
Ball milling with Na₂CO₃ achieves >95% copper extraction via water leaching. Reduces acid consumption 60%. No elevated temp required. Most immediately deployable.
Design for Degradation
PLA-PCBs: 95%+ binder + 100% fiberglass recovery. Vitrimer PCBs: full recyclability via transesterification. Transient electronics: dissolve in water in <10 minutes.

## Slide 5
Methodology
01
HMW Problem Framing
Defined scope: safer dismantling in Solapur using 12 Green Chemistry Principles (Anastas & Warner, 1998) as analytical framework.
02
Literature Search
Searched Chemical Reviews, Nature Energy, Journal of Hazardous Materials, Env. Pollution. 28 peer-reviewed sources synthesized.
03
Thematic Classification
Categorized studies under 3 pillars: Benign Solvents, Less Hazardous Synthesis, and Design for Degradation.
04
Critical Comparison
Compared methods for recovery efficiency, operational complexity, and suitability for Solapur's informal sector context.
05
Gap Identification
Identified absence of Indian-specific feedstock data and techno-economic analysis for informal sector conditions.
06
Synthesis & Recommendation
Proposed phased hybrid architecture: mechanochemical → DES → bioleaching, with nonmetallic fraction valorisation.

## Slide 6
Results: Metal Recovery Efficiency by Method
Chart: Metal Recovery Rate (%) by Process — Source: Amusa et al. 2026; Pathak et al. 2021; Guo et al. 2015
| Gold | Copper | Cobalt | Lithium | Silver
Deep Eutectic Solvents | 95 | 97 | 99.6 | 100 | 90
Bioleaching (Fungal) | 69 | 85 | 40 | 30 | 55
Mechanochemical | 60 | 95 | 50 | 35 | 58

## Slide 7
Results: Comparative Analysis
Chart: Typical PCB Material Composition by Mass
| Metals (Cu, Au, Ag, Pd) | Glass Fibre | Thermoset Resin | Other Polymers
PCB Composition | 28 | 30 | 25 | 17
Criteria | DES | Bioleaching | Mechanochem.
Precious metal recovery | 80-95% | 55-69% | ~60%
Base metal recovery | 90-100% | >80% | 95%
Toxic waste generated | Minimal | None | None
Deployment complexity | Medium | Medium-High | Low
Suitable for Solapur | Phase 2 | Phase 2-3 | Phase 1 ✓

## Slide 8
Key Studies in E-Waste Green Chemistry
Author(s) & Year | Method / System | Key Result | Relevance to Solapur
Amusa et al. (2026) | DES & Ionic Liquids review (150+ studies) | 100% Li, 99.6% Co, 95%+ Au/Cu recovery | Strongest evidence for DES adoption
Tran et al. / Nat. Energy (2019) | DES on Li-ion battery cathodes | >90% Co & Li; solvent regenerated 5+ cycles | Validates real-world multi-cycle use
Pathak et al. (2021) | Fungal bioleaching (Aspergillus niger) | 85% Cu at pH 4-6; 20% pulp density tolerated | Best near-term informal option; no acid dosing
Guo et al. (2015) | Ball milling + Na₂CO₃ mechanochemical | >95% Cu via water leaching at room temp | Phase 1 deployment; no liquid acid waste
Hubbard et al. / Nat. Sustain. (2024) | Vitrimer-based recyclable PCBs | Full recyclability; 11 env. categories reduced | Long-term design-for-degradation model
Sycheva et al. (2022) | PLA-substrate biodegradable PCBs | 95% PLA + 100% glass/Cu/components recovered | Near-zero hazardous by-products at EOL
Li et al. (2019) | Life cycle analysis of DES vs pyrometallurgy | 40-60% lower GWP; 70% lower acidification | Environmental case for switching to DES
Zhou et al. (2026) | Autocatalytic leaching (PMS/KCl aqueous) | 98.2% Au in 20 min, ambient temp, no catalyst | Safe ambient-temp Au recovery for informal use
Source: Synthesized from 28 peer-reviewed studies reviewed in this literature analysis (2001–2026)

## Slide 9
Discussion & Analysis
What Works
All three pillars (DES, bioleaching, mechanochemical) satisfy Green Chemistry Principles and eliminate open burning/acid leaching. DES achieves highest precious metal selectivity. Mechanochemical is most immediately deployable. Fungal bioleaching avoids strict pH control — ideal for informal Solapur operations.
Critical Gaps
No existing studies use Indian e-waste feedstock (Indian electronics differ in solder alloys and polymer substrate types). No techno-economic analysis exists for Indian informal sector cost structure. Solapur has zero published e-waste characterisation data — a direct opportunity for original research.
Recommended Path
Phased hybrid architecture: Phase 1 — mechanochemical pretreatment (ball milling). Phase 2 — DES for gold/silver. Phase 3 — fungal bioleaching for base metals. Nonmetallic fraction (70% of PCB mass) valorised as composite filler. E-Waste Management Rules 2022 provide regulatory support.

## Slide 10
Green chemistry solutions for safer e-waste dismantling in Solapur are technically validated, economically competitive, and policy-supported — the barrier is implementation, not technology.
1
Benign Solvents Proven
Deep eutectic solvents achieve 80-100% precious metal recovery with negligible toxicity under ambient conditions — ready for pilot in Solapur.
2
Safer Synthesis Exists
Fungal bioleaching and mechanochemical processing offer immediate entry points requiring no acid management, suitable for informal sector adoption.
3
Design for Degradation Advancing
PLA-PCBs and vitrimer-based boards enable near-zero-hazard end-of-life recovery. E-Waste Rules 2022 drive regulatory momentum for adoption.

## Slide 11
References
1. Amusa et al. (2026). Advances in metal recovery from e-waste: DES & ionic liquids. Sustainable Chemistry for the Environment, 13, 100307.
2. Alsafasfeh et al. (2026). Extraction of metals from waste PCBs via DES of organic acids. Journal of Sustainable Metallurgy.
3. Zhou et al. (2026). Green recovery of precious metals from e-waste via autocatalytic leaching. Angewandte Chemie.
4. Guo et al. (2024). Sustainable recovery of metals from e-waste using deep eutectic solvents. Separation and Purification Technology.
5. Hubbard et al. (2024). Recyclable vitrimer-based printed circuit boards. Nature Sustainability.
6. Sycheva et al. (2022). A new approach to designing easily recyclable PCBs. Scientific Reports, 12, 22254.
7. Forti et al. (2020). The Global E-waste Monitor 2020. United Nations University, Bonn.
8. Tran et al. (2019). Deep eutectic solvents for cathode recycling of Li-ion batteries. Nature Energy, 4, 339-345.
9. Smith et al. (2014). Deep eutectic solvents (DESs) and their applications. Chemical Reviews, 114(21), 11060-11082.
10. Jenkin et al. (2016). DES ionic liquids for dissolution and recovery of precious metals. Minerals Engineering, 87, 18-24.
11. Pathak et al. (2021). Fungal bioleaching of e-waste. Journal of Hazardous Materials.
12. Anastas, P.T.; Warner, J.C. (1998). Green Chemistry: Theory and Practice. Oxford University Press.
13. Awasthi et al. (2016). Environmental pollution of electronic waste recycling in India. Environmental Pollution, 211, 259-270.
14. Annamalai (2015). Occupational health hazards related to informal recycling of e-waste in India. Indian Journal of Occupational Medicine, 19(1), 61-65.
15. Guo et al. (2015). Mechanochemical copper extraction from PCBs. Resources, Conservation and Recycling.
16. Ilyas et al. (2010). Bacterial bioleaching: 80%+ Cu via mixed acidophilic consortia. Bioresource Technology.
17. Cui & Zhang (2008). Metallurgical recovery of metals from electronic waste. Journal of Hazardous Materials, 158, 228-256.
18. Brandl et al. (2001). Bioleaching proof of concept from PCBs. Journal of Hazardous Materials.

## Slide 12
Thank You
Questions & Discussion
Applied Chemistry for Engineers (AS-1201)
B.Tech CSE-AIML | Solapur, Maharashtra
Instructor: Prof. Veeranna Yempally | February 2026

## Slide 13
Health & Environmental Hazards of Informal Dismantling
Toxic Heavy Metals
Pb, Cd, Hg, Cr, As released during acid stripping & incineration
Respiratory Disease
Open burning releases dioxins (PCDD/F) — 10-100× above safe thresholds (Huang et al., 2009)
Neurological Damage
Blood lead levels in informal workers measured 3–10× safe reference values (Sthiannopkao & Wong, 2013)
Soil & Water Pollution
Heavy metal concentrations in soil exceed WHO guidelines by 10–1,000× (Awasthi et al., 2016)
Exposure Pathways
Incineration
& Burning
Acid
Leaching
Manual
Disassembly
Improper
Dumping
Worker & Community
Health Impacts
25,000 workers in Delhi alone dismantle 10,000–20,000 tonnes of e-waste annually with bare hands (Palanivel & Sulaiman, 2014)

## Slide 14
Analytical Framework: 12 Green Chemistry Principles
Anastas & Warner (1998) — evaluative lens for all three solution pillars in this review
P1
Waste Prevention
P2
Atom Economy
P3
Less Hazardous Synthesis
P4
Safer Products
P5
Safer Solvents
P6
Energy Efficiency
P7
Renewable Feedstocks
P8
Avoid Derivatives
P9
Catalysis
P10
Design for Degradation
P11
Real-time Monitoring
P12
Inherently Safer Chemistry
Principles directly applied in this review
Not the primary focus of this review

## Slide 15
Deep Dive: Deep Eutectic Solvents (DES)
How DES Systems Work
Hydrogen Bond
Acceptor (HBA)
e.g. Choline Chloride
+
Hydrogen Bond
Donor (HBD)
e.g. Urea, Oxalic Acid
→
Deep Eutectic
Solvent (DES)
Low melting point, stable liquid
Key Properties of DES vs Conventional Solvents
Property | DES | Cyanide / Aqua Regia
Toxicity | Low — food-grade precursors | Extremely high
Biodegradability | Yes — fully biodegradable | No — persistent pollutant
Operating temperature | Ambient (25–80°C) | High (100–200°C for pyro)
Au recovery rate | 80–95% | 90–98% (but hazardous)
GWP vs pyrometallurgy | 40–60% lower | Baseline (high)
Landmark Studies
Smith et al. (2014)
Foundational DES chemistry review — 5,400+ citations. Established biodegradable, food-grade synthesis route.
Jenkin et al. (2016)
80–95% gold & silver dissolution from mixed metals at ambient temperature. No cyanide.
Tran et al. (2019)
Nature Energy
>90% Co & Li from real Li-ion battery cathodes. Solvent regenerated across 5+ cycles.
Amusa et al. (2026)
150+ study meta-review confirms 100% Li, 99.6% Co, 95%+ Au/Cu under optimised DES conditions.

## Slide 16
Deep Dive: Bioleaching — Bacterial vs. Fungal Routes
Bacterial Bioleaching
Organism(s):
Acidithiobacillus ferrooxidans
Chromobacterium violaceum
Mechanism:
Enzymatic oxidation at acidic pH
(1.5–2.5)
Cu Recovery
80–95%
Au Recovery
55–69%
Advantages
High peak copper recovery
Well-documented in literature
Scalable in column reactor configs
Limitations
Strict pH maintenance required
Long process time (~70 days)
Challenging for informal ops without pH monitoring
Fungal Bioleaching
Organism(s):
Aspergillus niger
Penicillium simplicissimum
Mechanism:
Citric & gluconic acid production
at near-neutral pH (4–6)
Cu Recovery
85%
Au Recovery
~40–55%
Advantages
Near-neutral pH — no acid dosing needed
Tolerates 20% pulp density
More accessible for informal settings
Limitations
Slightly lower peak recovery than bacterial
Requires incubation infrastructure
Longer culture preparation time
Verdict for Solapur: Fungal bioleaching is the realistic near-term entry point — no acid dosing, tolerates high pulp density, and requires only incubation infrastructure.

## Slide 17
India's E-Waste Policy Landscape
2011
E-Waste (Management & Handling) Rules
First dedicated Indian e-waste legislation. Mandated Extended Producer Responsibility (EPR) and authorized recycler network.
2016
E-Waste Management Rules (Revised)
Strengthened EPR framework. Set producer collection targets. Introduced deposit-refund scheme. Maharashtra among first states to attempt enforcement.
2022
E-Waste Management Rules 2022
Most significant update. Producer recovery targets scaled from 25% to 70% over 4 years. Mandates formal recycler channelization for Tier-2 cities including Solapur.
2023+
Enforcement & Compliance Phase
State-level PCBs (Pollution Control Boards) tasked with annual compliance audits. Non-compliant producers face penalties up to ₹1 crore.
Key insight: E-Waste Rules 2022 create regulatory PUSH (compliance pressure) while DES/bioleaching economics create financial PULL — together these open the window for Solapur formalisation.

## Slide 18
Phased Implementation Roadmap for Solapur
Phase 1
(0–6 months)
01
Mechanochemical Pretreatment
Ball milling with Na₂CO₃ — no acids
>95% Cu via water leaching at room temp
Ball milling equipment available in Maharashtra's industrial supply chain
Minimal training required
Phase 2
(6–18 months)
02
DES Gold & Silver Recovery
Deploy choline chloride / oxalic acid DES
80–95% Au/Ag recovery from mechanically pre-treated feedstock
Establish solvent recovery loop for economic sustainability
Worker training on low-hazard chemistry
Phase 3
(18–36 months)
03
Fungal Bioleaching for Base Metals
Add Aspergillus niger bioleaching for Cu/Ni residues
Near-neutral pH — no continuous acid dosing
Nonmetallic fraction (70% PCB mass) valorised as composite filler
Full hybrid circuit complete
All phases align with E-Waste Management Rules 2022 | Satisfies Green Chemistry Principles 3, 5, 7, 10, 12 | No phase requires open burning or cyanide

## Slide 19
Research Gaps & Future Work
Critical gaps identified — each represents a direct opportunity for original applied chemistry research
CRITICAL
Indian Feedstock Characterisation
All reviewed bioleaching and DES studies use European or generalised feedstock. Indian consumer electronics differ in solder alloy composition and polymer substrate type. Whether published recovery efficiencies translate to Indian feedstock is entirely unestablished.
Proposed study: Characterise Solapur e-waste stream composition, then run DES and bioleaching trials on local feedstock.
CRITICAL
Techno-Economic Analysis for Informal Sector
No cost-benefit study exists for DES or bioleaching implementation at the scale and infrastructure level of Solapur's informal clusters. Cucchiella et al. (2015) established green chemistry reduces costs by 30–40% vs conventional processing — but this was not for Indian informal operations.
Proposed study: Model capital and operating costs for a 5 tonne/day mechanochemical + DES pilot at a Solapur cluster.
HIGH
Solapur-Specific Health Impact Assessment
No published occupational health data exists for Solapur's informal e-waste workforce specifically. Delhi and Mumbai studies cannot be assumed representative of Solapur's operations, workforce profile, or chemical exposure patterns.
Proposed study: Blood heavy metal screening + occupational health survey for informal dismantlers in Solapur.
HIGH
E-Waste Rules 2022 Enforcement Analysis
Garlapati (2016) documented state-level policy inconsistency as the binding constraint on e-waste formalisation in India. Whether E-Waste Rules 2022 enforcement mechanisms reach Tier-2 cities like Solapur has not been studied.
Proposed study: Interview-based analysis of EPR compliance audit reach in Maharashtra Tier-2 cities.